## Slide 1: CS162 Operating Systems and Systems Programming Lecture 8 Synchronization 2: Lock Implementation, Atomic Instructions, Futex, Need for Higher-Level Locking
February 8th, 2024
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Multiple Threads on One CPU/core
Thread T's switch returns to Thread S
[ Thread T on Ready queue,
Thread S is Running ]
Consider the following code blocks:
proc A() {
B();
}
proc B() {
while(TRUE) {
yield();
}
}
Suppose we have 2 threads:
  Threads S and T
Kernel stack contains pointers to all state and can be placed on any queue:
  Ready queue – available to run again
  Some wait queue – won’t run again until condition resolved and back on ready queue
Thread S
Stack growth
A
B(while)
yield
run_new_thread
Thread T
A
B(while)
yield
run_new_thread
switch
switch
kernel_yield
kernel_yield

## Slide 3: Recall: Fix banking problem with Locks!
Thread C
Identify critical sections (atomic instruction sequences) and add locking:
Deposit(acctId, amount) {
acquire(&mylock) // Wait if someone else in critical section! acct = GetAccount(actId); acct->balance += amount; StoreAccount(acct);
release(&mylock) // Release someone into critical section }
Must use SAME lock (mylock) with all of the methods (Withdraw, etc…)
  Shared with all threads!
Thread A
Thread B
Thread A
Thread A
Thread C
Thread B
Thread B
Critical Section
acquire(&mylock)
release(&mylock)
Critical Section
Threads serialized by lock through critical section.
Only one thread at a time

## Slide 4: Today’s Motivating Example: “Too Much Milk”
Great thing about OS’s – analogy between problems in OS and problems in real life
  Help you understand real life problems better
  But, computers are much stupider than people
Example: People need to coordinate:
Arrive home, put milk away
3:30
Buy milk
3:25
Arrive at store
Arrive home, put milk away
3:20
Leave for store
Buy milk
3:15
Leave for store
3:05
Look in Fridge. Out of milk
3:00
Look in Fridge. Out of milk
Arrive at store
3:10
Person B
Person A
Time
Notes: You’re sitting in class, hot day, milk does a body good. Go home, no milk, so go to store
Roommate leaves class late because prof is more long-winded than I am. Has same idea, but result is too much milk!
Problem: two cooperating threads, not cooperating properly

## Slide 5: Solve with a lock?
Recall: Lock prevents someone from doing something
  Lock before entering critical section
  Unlock when leaving
  Wait if locked
    Important idea: all synchronization involves waiting
For example: fix the milk problem by putting a key on the refrigerator
  Lock it and take key if you are going to go buy milk
  Fixes too much: roommate angry if only wants OJ
Of Course – We don’t know how to make a lock yet
  Let’s see if we can answer this question!
#$@%@#$@

## Slide 6: Too Much Milk: Correctness Properties
Need to be careful about correctness of concurrent programs, since non-deterministic
  Impulse is to start coding first, then when it doesn’t work, pull hair out
  Instead, think first, then code
  Always write down behavior first
What are the correctness properties for the “Too much milk” problem???
  Never more than one person buys
  Someone buys if needed
First attempt: Restrict ourselves to use only atomic load and store operations as building blocks

## Slide 7: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
  if (noMilk) { if (noNote) { leave Note; buy milk; remove note; } }
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 8: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
Thread A Thread B
if (noMilk) { if (noMilk) { if (noNote) {
if (noNote) { leave Note;
buy Milk;
remove Note;
}
}
leave Note;
buy Milk;
remove Note; } }
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 9: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
  if (noMilk) { if (noNote) { leave Note; buy milk; remove note; } }
Result?
  Still too much milk but only occasionally!
  Thread can get context switched after checking milk and note but before buying milk!
Solution makes problem worse since fails intermittently
  Makes it really hard to debug…
  Must work despite what the dispatcher does!
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 10: Too Much Milk: Solution #1½
Clearly the Note is not quite blocking enough
  Let’s try to fix this by placing note first
Another try at previous solution:
  leave Note;
  if (noMilk) { if (noNote) { buy milk; } }
  remove Note;
What happens here?
  Well, with human, probably nothing bad
  With computer: no one ever buys milk

## Slide 11: Too Much Milk Solution #2
How about labeled notes?
  Now we can leave note before checking
Algorithm looks like this:
Thread A Thread B
leave note A; leave note B; if (noNote B) { if (noNoteA) { if (noMilk) { if (noMilk) { buy Milk; buy Milk; } } } } remove note A; remove note B;
Does this work?
Possible for neither thread to buy milk
  Context switches at exactly the wrong times can lead each to think that the other is going to buy
Really insidious:
  Extremely unlikely this would happen, but will at worse possible time
  Probably something like this in UNIX

## Slide 12: Too Much Milk Solution #2: problem!
I’m not getting milk, You’re getting milk
This kind of lockup is called “starvation!”

## Slide 13: Too Much Milk Solution #3
Here is a possible two-note solution:
Thread A Thread B
leave note A; leave note B; while (note B) {\\X if (noNote A) {\\Y do nothing; if (noMilk) { } buy milk; if (noMilk) { } buy milk; } } remove note B; remove note A;
Does this work? Yes. Both can guarantee that:
  It is safe to buy, or
  Other will buy, ok to quit
At X:
  If no note B, safe for A to buy,
  Otherwise wait to find out what will happen
At Y:
  If no note A, safe for B to buy
  Otherwise, A is either buying or waiting for B to quit

## Slide 14: Case 1
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“leave note A” happens before “if (noNote A)”

## Slide 15: Case 1
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
“leave note A” happens before “if (noNote A)”

## Slide 16: Case 1
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
Wait for note B to be removed
happened
before
“leave note A” happens before “if (noNote A)”

## Slide 17: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”

## Slide 18: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”

## Slide 19: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”
Wait for note B to be removed

## Slide 20: This Generalizes to Threads…
Leslie Lamport’s “Bakery Algorithm” (1974)

## Slide 21: Solution #3 discussion
Our solution protects a single “Critical-Section” piece of code for each thread:
if (noMilk) { buy milk; }
Solution #3 works, but it’s really unsatisfactory
  Really complex – even for this simple an example
    Hard to convince yourself that this really works
  A’s code is different from B’s – what if lots of threads?
    Code would have to be slightly different for each thread
  While A is waiting, it is consuming CPU time
    This is called “busy-waiting”
There’s got to be a better way!
  Have hardware provide higher-level primitives than atomic load & store
  Build even higher-level programming abstractions on this hardware support

## Slide 22: Too Much Milk: Solution #4?
Recall our target lock interface:
  acquire(&milklock) – wait until lock is free, then grab
  release(&milklock) – Unlock, waking up anyone waiting
  These must be atomic operations – if two threads are waiting for the lock and both see it’s free, only one succeeds to grab the lock
Then, our milk problem is easy:
acquire(&milklock);
if (nomilk)
buy milk;
release(&milklock);

## Slide 23: Where are we going with synchronization?
Hardware
Higher-level API
Programs
We are going to implement various higher-level synchronization primitives using atomic operations
  Everything is pretty painful if only atomic primitives are load and store
  Need to provide primitives useful at user-level
Load/Store Disable Ints Test&Set Compare&Swap
Locks Semaphores Monitors Send/Receive
Shared Programs

## Slide 24: Administrivia
Midterm Next Thursday (February 15, 8-10pm)!
  No class on day of midterm (extra office hours during class time)
  Topics, lectures, and assignments up to an including next Tuesday
  Closed book, one page of handwritten notes allowed
Project 1 Design Document Due Date Saturday
Project 1 Design reviews upcoming
  High-level discussion of your approach
    What will you modify?
    What algorithm will you use?
    How will things be linked together, etc.
    Do not need final design (complete with all semicolons!)
  You will be asked about testing
    Understand testing framework
    Are there things you are doing that are not tested by tests we give you?

## Slide 25: Back to: How to Implement Locks?
Lock: prevents someone from doing something
  Lock before entering critical section and before accessing shared data
  Unlock when leaving, after accessing shared data
  Wait if locked
    Important idea: all synchronization involves waiting
    Should sleep if waiting for a long time
Atomic Load/Store: get solution like Milk #3
  Pretty complex and error prone
Hardware Lock instruction
  Is this a good idea?
  What about putting a task to sleep?
    What is the interface between the hardware and scheduler?
  Complexity?
    Done in the Intel 432
    Each feature makes HW more complex and slow

## Slide 26: Naïve use of Interrupt Enable/Disable
How can we build multi-instruction atomic operations?
  Recall: dispatcher gets control in two ways.
    Internal: Thread does something to relinquish the CPU
    External: Interrupts cause dispatcher to take CPU
  On a uniprocessor, can avoid context-switching by:
    Avoiding internal events (although virtual memory tricky)
    Preventing external events by disabling interrupts
Consequently, naïve Implementation of locks: LockAcquire { disable Ints; } LockRelease { enable Ints; }
Problems with this approach:
  Can’t let user do this! Consider following:
    LockAcquire(); While(TRUE) {;}
  Real-Time system—no guarantees on timing!
    Critical Sections might be arbitrarily long
  What happens with I/O or other important events?
    “Reactor about to meltdown. Help?”

## Slide 27: Better Implementation of Locks by Disabling Interrupts
int value = FREE;
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); // Enable interrupts? } else { value = BUSY; } enable interrupts; }
Release() { disable interrupts; if (anyone on wait queue) { take thread off wait queue Place on ready queue; } else { value = FREE; } enable interrupts; }
Key idea: maintain a lock variable and impose mutual exclusion only during operations on that variable

## Slide 28: New Lock Implementation: Discussion
Why do we need to disable interrupts at all?
  Avoid interruption between checking and setting lock value.
  Prevent switching to other thread that might be trying to acquire lock!
  Otherwise two threads could think that they both have lock!
Note: unlike previous solution, this “meta-”critical section is very short
  User of lock can take as long as they like in their own critical section: doesn’t impact global machine behavior
  Critical interrupts taken in time!
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); // Enable interrupts? } else { value = BUSY; } enable interrupts; }
“Meta-” Critical
Section

## Slide 29: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }

## Slide 30: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position?

## Slide 31: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position?

## Slide 32: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position?

## Slide 33: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
  Release puts the thread on the ready queue, but the thread still thinks it needs to go to sleep
  Misses wakeup and still holds lock (deadlock!)
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position?

## Slide 34: What about Interrupt Re-enable in Going to Sleep?
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
  Release puts the thread on the ready queue, but the thread still thinks it needs to go to sleep
  Misses wakeup and still holds lock (deadlock!)
Want to put it after sleep(). But – how?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position?

## Slide 35: How to Re-enable After Sleep()?
In scheduler, since interrupts are disabled when you call sleep:
  Responsibility of the next thread to re-enable ints
  When the sleeping thread wakes up, returns to acquire and re-enables interrupts
  Thread A Thread B
  . . disable ints sleep
  sleep return enable ints
  . . .
  disable int sleep
  sleep return enable ints . .
context switch
context switch

## Slide 36: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Value: 0
waiters
owner
Thread A
Thread B
Running
READY
Ready

## Slide 37: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready

## Slide 38: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 39: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 40: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 41: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Running
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 42: Atomic Read-Modify-Write Instructions
Problems with previous solution:
  Can’t give lock implementation to users
  Doesn’t work well on multiprocessor
    Disabling interrupts on all processors requires messages and would be very time consuming
Alternative: atomic instruction sequences
  These instructions read a value and write a new value atomically
  Hardware is responsible for implementing this correctly
    on both uniprocessors (not too hard)
    and multiprocessors (requires help from cache coherence protocol)
  Unlike disabling interrupts, can be used on both uniprocessors and multiprocessors

## Slide 43: Examples of Read-Modify-Write
test&set (&address) { /* most architectures */ result = M[address]; // return result from “address” and M[address] = 1; // set value at “address” to 1 return result; }
swap (&address, register) { /* x86 */ temp = M[address]; // swap register’s value to M[address] = register; // value at “address” register = temp; // value from “address” put back to register return temp; // value from “address” considered return from swap }
compare&swap (&address, reg1, reg2) { /* x86 (returns old value), 68000 */ if (reg1 == M[address]) { // If memory still == reg1, M[address] = reg2; // then put reg2 => memory return success; } else { // Otherwise do not change memory return failure; } }
load-linked&store-conditional(&address) { /* R4000, alpha */ loop: ll r1, M[address]; movi r2, 1; // Can do arbitrary computation sc r2, M[address]; beqz r2, loop; }

## Slide 44: Using of Compare&Swap for queues
compare&swap (&address, reg1, reg2) { /* x86, 68000 */ if (reg1 == M[address]) { M[address] = reg2; return success; } else { return failure; } }
Here is an atomic add to linkedlist function:
addToQueue(&object) { do { // repeat until no conflict ld r1, M[root] // Get ptr to current head st r1, M[object] // Save link in new object } until (compare&swap(&root,r1,object)); }
root
next
next
next
New
Object

## Slide 45: Implementing Locks with test&set
Simple lock that doesn’t require entry into the kernel:
// (Free) Can access this memory location from user space! int mylock = 0; // Interface: acquire(&mylock); // release(&mylock);
acquire(int *thelock) { while (test&set(thelock)); // Atomic operation! }
release(int *thelock) { *thelock = 0; // Atomic operation! }
Simple explanation:
  If lock is free, test&set reads 0 and sets lock=1, so lock is now busy. It returns 0 so while exits.
  If lock is busy, test&set reads 1 and sets lock=1 (no change) It returns 1, so while loop continues.
  When we set thelock = 0, someone else can get lock.
Busy-Waiting: thread consumes cycles while waiting
  For multiprocessors: every test&set() is a write, which makes value ping-pong around in cache (using lots of network BW)

## Slide 46: Problem: Busy-Waiting for Lock
Positives for this solution
  Machine can receive interrupts
  User code can use this lock
  Works on a multiprocessor
Negatives
  This is very inefficient as thread will consume cycles waiting
  Waiting thread may take cycles away from thread holding lock (no one wins!)
  Priority Inversion: If busy-waiting thread has higher priority than thread holding lock  no progress!
Priority Inversion problem with original Martian rover
For higher-level synchronization primitives (e.g. semaphores or monitors), waiting thread may wait for an arbitrary long time!
  Thus even if busy-waiting was OK for locks, definitely not ok for other primitives
  Homework/exam solutions should avoid busy-waiting!

## Slide 47: Multiprocessor Spin Locks: test&test&set
A better solution for multiprocessors:
// (Free) Can access this memory location from user space! int mylock = 0; // Interface: acquire(&mylock); // release(&mylock);
acquire(int *thelock) {
do {
while(*thelock); // Wait until might be free (quick check/test!) } while(test&set(thelock)); // Atomic grab of lock (exit if succeeded)
}
release(int *thelock) { *thelock = 0; // Atomic release of lock }
Simple explanation:
  Wait until lock might be free (only reading – stays in cache)
  Then, try to grab lock with test&set
  Repeat if fail to actually get lock
Issues with this solution:
  Busy-Waiting: thread still consumes cycles while waiting
    However, it does not impact other processors!

## Slide 48: Better Locks using test&set
Can we build test&set locks without busy-waiting?
  Mostly. Idea: only busy-wait to atomically check lock value
Note: sleep has to be sure to reset the guard variable
  Why can’t we do it just before or just after the sleep?
release(int *thelock) { // Short busy-wait time while (test&set(guard)); if anyone on wait queue { take thread off wait queue Place on ready queue; } else { *thelock = FREE; } guard = 0;
int guard = 0; // Global Variable!
int mylock = FREE; // Interface: acquire(&mylock); // release(&mylock);
acquire(int *thelock) {
// Short busy-wait time while (test&set(guard)); if (*thelock == BUSY) {
put thread on wait queue;
go to sleep() & guard = 0;
// guard == 0 on wakup! } else { *thelock = BUSY; guard = 0; } }

## Slide 49: Recap: Locks using interrupts
acquire(int *thelock) {
// Short busy-wait time disable interrupts; if (*thelock == 1) {
put thread on wait-queue;
go to sleep() //?? } else { *thelock = 1; enable interrupts; } }
release(int *thelock) { // Short busy-wait time disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { *thelock = 0; } enable interrupts; }
int mylock=0;
acquire(&mylock);
…
critical section;
…
release(&mylock);
acquire(int *thelock) {
disable interrupts; }
release(int *thelock) { enable interrupts; }
If one thread in critical section, no other activity (including OS) can run!
Lock argument not used!

## Slide 50: Recap: Locks using test & set
int guard = 0; // global!
acquire(int *thelock) {
// Short busy-wait time while(test&set(guard)); if (*thelock == 1) {
put thread on wait-queue;
go to sleep()& guard = 0;
// guard == 0 on wakeup } else { *thelock = 1; guard = 0; } }
release(int *thelock) { // Short busy-wait time while (test&set(guard)); if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { *thelock = 0; } guard = 0; }
int mylock=0;
acquire(&mylock);
…
critical section;
…
release(&mylock);
int mylock = 0;
acquire(int *thelock) {
while(test&set(thelock)); }
release(int *thelock) { *thelock = 0; }
Threads waiting to enter critical section busy-wait

## Slide 51: Linux futex: Fast Userspace Mutex
uaddr points to a 32-bit value in user space
futex_op
  FUTEX_WAIT – if val == *uaddr sleep till FUTEX_WAIT
    Atomic check that condition still holds after we disable interrupts (in kernel!)
  FUTEX_WAKE – wake up at most val waiting threads
  FUTEX_FD, FUTEX_WAKE_OP, FUTEX_CMP_REQUEUE: More interesting operations!
timeout
  ptr to a timespec structure that specifies a timeout for the op
Interface to the kernel sleep() functionality!
  Let thread put themselves to sleep – conditionally!
futex is not exposed in libc; it is used within the implementation of pthreads
  Can be used to implement locks, semaphores, monitors, etc…
#include <linux/futex.h>
#include <sys/time.h>
int futex(int *uaddr, int futex_op, int val,
const struct timespec *timeout );

## Slide 52: Example: First try: T&S and futex
Properties:
  Sleep interface by using futex – no busywaiting
No overhead to acquire lock
  Good!
Every unlock has to call kernel to potentially wake someone up – even if none
  Doesn’t quite give us no-kernel crossings when uncontended…!
int mylock = 0; // Interface: acquire(&mylock);
// release(&mylock);
acquire(int *thelock) {
while (test&set(thelock)) {
futex(thelock, FUTEX_WAIT, 1);
} }
release(int *thelock) {
*thelock = 0; // unlock futex(thelock, FUTEX_WAKE, 1);
}

## Slide 53: Example: Try #2: T&S and futex
This is syscall-free in the uncontended case
  Temporarily falls back to syscalls if multiple waiters, or concurrent acquire/release
But it can be considerably optimized!
  See “Futexes are Tricky” by Ulrich Drepper
release(int *thelock, bool *maybe) { *thelock = 0;
if (*maybe) {
*maybe = false;
// Try to wake up someone
futex(thelock, FUTEX_WAKE, 1);
} }
bool maybe_waiters = false;
int mylock = 0; // Interface: acquire(&mylock,&maybe_waiters);
// release(&mylock,&maybe_waiters);
acquire(int *thelock, bool *maybe) {
while (test&set(thelock)) {
// Sleep, since lock busy!
*maybe = true;
futex(thelock, FUTEX_WAIT, 1);
// Make sure other sleepers not stuck
*maybe = true;
} }

## Slide 54: Try #3: Better, using more atomics
Much better: Three (3) states:
  UNLOCKED: No one has lock
  LOCKED: One thread has lock
  CONTESTED: Possibly more than one (with someone sleeping)
Clean interface!
Lock grabbed cleanly by either
  compare&swap()
  First swap()
No overhead if uncontested!
Could build semaphores in a similar way!
typedef enum { UNLOCKED,LOCKED,CONTESTED } Lock;
Lock mylock = UNLOCKED; // Interface: acquire(&mylock);
// release(&mylock);
acquire(Lock *thelock) {
// If unlocked, grab lock!
if (compare&swap(thelock,UNLOCKED,LOCKED))
return;
// Keep trying to grab lock, sleep in futex
while (swap(thelock,CONTESTED) != UNLOCKED))
// Sleep unless someone releases here!
futex(thelock, FUTEX_WAIT, CONTESTED);
}
release(Lock *thelock) {
// If someone sleeping, if (swap(thelock,UNLOCKED) == CONTESTED)
futex(thelock,FUTEX_WAKE,1); }

## Slide 55: Recall: Where are we going with synchronization?
Hardware
Higher-level API
Programs
We are going to implement various higher-level synchronization primitives using atomic operations
  Everything is pretty painful if only atomic primitives are load and store
  Need to provide primitives useful at user-level
Load/Store Disable Ints Test&Set Compare&Swap
Locks Semaphores Monitors Send/Receive
Shared Programs

## Slide 56: Producer-Consumer with a Bounded Buffer
Problem Definition
  Producer(s) put things into a shared buffer
  Consumer(s) take them out
  Need synchronization to coordinate producer/consumer
Don’t want producer and consumer to have to work in lockstep, so put a fixed-size buffer between them
  Need to synchronize access to this buffer
  Producer needs to wait if buffer is full
  Consumer needs to wait if buffer is empty
Example 1: GCC compiler
  cpp | cc1 | cc2 | as | ld
Example 2: Coke machine
  Producer can put limited number of Cokes in machine
  Consumer can’t take Cokes out if machine is empty
Others: Web servers, Routers, ….
Consumer
Consumer
Producer
Consumer
Buffer
Producer

## Slide 57: Bounded Buffer Data Structure (sequential case)
Insert: write & bump write ptr (enqueue)
Remove: read & bump read ptr (dequeue)
How to tell if Full (on insert) Empty (on remove)?
And what do you do if it is?
What needs to be atomic?
typedef struct buf {
int write_index;
int read_index;
<type> *entries[BUFSIZE];
} buf_t;
w
r
di
di+1
di+2

## Slide 58: Bounded Buffer – first cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {}; // Wait for a free slot
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {}; // Wait for arrival
item = dequeue(); release(&buf_lock);
return item
}
Will we ever come out of the wait loop?

## Slide 59: Bounded Buffer – 2nd cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {release(&buf_lock); acquire(&buf_lock);}
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {release(&buf_lock); acquire(&buf_lock);}
item = dequeue(); release(&buf_lock);
return item
}
What happens when one is waiting for the other?
- Multiple cores ?
- Single core ?


## Slide 60: Higher-level Primitives than Locks
Goal of last couple of lectures:
  What is right abstraction for synchronizing threads that share memory?
  Want as high a level primitive as possible!
Good primitives and practices important!
  Since execution is not entirely sequential, really hard to find bugs, since they happen rarely
  UNIX is pretty stable now, but up until about mid-80s (10 years after started), systems running UNIX would crash every week or so – concurrency bugs
Synchronization is a way of coordinating multiple concurrent activities that are using shared state
  This lecture and the next presents a some ways of structuring sharing

## Slide 61: Summary
Important concept: Atomic Operations
  An operation that runs to completion or not at all
  These are the primitives on which to construct various synchronization primitives
Talked about hardware atomicity primitives:
  Disabling of Interrupts, test&set, swap, compare&swap, load-locked & store-conditional
Showed several constructions of Locks
  Must be very careful not to waste/tie up machine resources
    Shouldn’t disable interrupts for long
    Shouldn’t spin wait for long
  Key idea: Separate lock variable, use hardware mechanisms to protect modifications of that variable
Showed primitive for constructing user-level locks
  Packages up functionality of sleeping